## Slide 1: Particle Filtering for Localization
Information Processing In Autonomous Systems
Yarin Hausler

## Slide 2: Abstract
Particle filtering is a powerful probabilistic method for state estimation in dynamic systems. In this presentation, we investigate the application of particle filtering for localization of an agent in a beacon-based environment. We present a perception algorithm, specifically, an adaptive particle filter, that effectively estimates the agent's whereabouts in the field.

## Slide 3: Introduction
The goal of this study is to design a perception algorithm that enables an agent to estimate its location in a field containing beacons with known coordinates. The agent's perception is limited to a proximity sensor and an odometer, and it lacks knowledge of its true location. The effectiveness of the algorithm is assessed through simulation and analysis.

## Slide 4: The Real World
The real world is a Euclidean plane within which the beacons are located. It is represented by the set of beacon locations together with the coordinates A and B, representing the terminal points of a trajectory to be followed by the agent. The beacon coordinates, the real numbers, (Xi, Yi), i = 1,…,Nb, are independently drawn from a uniform density over a rectangular region with the corners (0, 0) and (EndX, EndY).

## Slide 5: The World Perceived by the Agent
The agent state at time k, denoted z_k, is its instantaneous location in the real world, i.e., some point along the trajectory we have generated for it. The agent itself is unaware of its actual location and so it tries to estimate it using nearby beacon locations. The agent perceives the world only through its sensors, a very limited proximity sensor and an odometer. In addition, it is provided with the set of beacon locations (X_i, Y_i) and their identities. The proximity sensor is able to identify a beacon and measure its distance from the agent. Its reading is a set of beacon identifiers and their measured distances beacon_distance within a radius of 2 from the actual agent's location.

## Slide 6: Perception (Information Fusion) Algorithm
The information fusion, or estimation, algorithm is a particle filter aimed at estimating the agent's state, z_k, based on the set of nearby beacons up to time k. To implement the particle filter, we first need to perform a several steps:
Prediction
Update
Likelihoods and weights update
Resampling / ESS
Estimation

## Slide 7: Pseudo-Code for Particle Filtering Algorithm

## Slide 8: Pseudo-Code for Particle Filtering Algorithm

## Slide 9: Pseudo-Code for Particle Filtering Algorithm

## Slide 10: Pseudo-Code for Particle Filtering Algorithm

## Slide 11: The Effect of the Number of Particles
Agent trajectory and Estimated position (1000 particles, 10 beacons, end at [4,8]):
Total MSE: 0.07

## Slide 12: The Effect of the Number of Particles
Mean squared estimation error over time (1000 particles, 10 beacons, end at [4,8]):
Total MSE: 0.07

## Slide 13: The Effect of the Number of Particles
Mean squared estimation error over time (2000 particles, 10 beacons, end at [4,8]):
Total MSE: 0.045

## Slide 14: The Effect of the Number of Particles
Mean squared estimation error over time (4000 particles, 10 beacons, end at [4,8]):
Total MSE: 0.05

## Slide 15: The Effect of the Number of Particles
Mean squared estimation error over time (8000 particles, 10 beacons, end at [4,8]):
Total MSE: 0.04

## Slide 16: The Effect of the ESS
Agent trajectory and Estimated position (1000 particles, 10 beacons, end at [3,10]):
ESS ‘OFF’: Total MSE = 0.062 ESS ‘ON’: Total MSE = 0.0324

## Slide 17: The Effect of the ESS
Agent trajectory and Estimated position (1000 particles, 10 beacons, end at [4,9]):
ESS ‘OFF’: Total MSE = 0.0679 ESS ‘ON’: Total MSE = 0.0594

## Slide 18: Thank You!